## Slide 1: How-to Implement a DFT on a Real-Time System
Rainer Nitsche – 02/2024
Discrete Fourier Transform – DFT

## Slide 2: FFT/DFT in Real-Time | Objectives
Analyzing a time domain signal in the frequency domain ⇝ Fourier Transform
The fast Fourier transform (FFT) is an efficient method to compute a discrete Fourier transform (DFT)
Example
Parameters:
Time ->
f
FFT DFT

## Slide 3: FFT/DFT in Real-Time | Discrete Fourier Transform (DFT)
Discrete-time signal
Multiplication with sines and cosines of different frequencies
See also: https://www.youtube.com/watch?v=QmgJmh2I3Fw
DFT: Matrix Multiplication
N: number of samples
0 1 2 . . .
N-1
k
positive
negative
Notes: https://www.overleaf.com/learn/latex/Using_colors_in_LaTeX
Skalarprodukt oder inneres Produkt von xn mit der k-ten Spalte…
Für große N wird die Multiplikation sehr aufwändig -> FFT
k: Frequenz
n: sample Point -> time
X[k]: correlating signal

## Slide 4: FFT in Real-Time | Practical Issues: one- / two-sided FFT
One-sided and two-sided FFT
Nyquist frequency
K=0
K=N-1
positive
negative
Nyquist frequency:
Notes: Positive and negative Frequenzen in der FFT

## Slide 5: FFT in Real-Time | Practical Issues: one- / two-sided FFT
One-sided and two-sided FFT
Nyquist frequency
K=0
K=N-1
positive
negative
Notes: Positive and negative Frequenzen in der FFT

## Slide 6: FFT in Real-Time | Practical Issues: one- / two-sided FFT
One-sided and two-sided FFT
Nyquist frequency
K=0
positive
negative
two-sided
Notes: Positive and negative Frequenzen in der FFT

## Slide 7: FFT in Real-Time | Practical Issues: one- / two-sided FFT
One-sided and two-sided FFT
Nyquist frequency
K=0
positive
one-sided
Nyquist frequency:
Nyquist frequency is the highest frequency which can be measured / detected in the
sampled data
0 1 2 . . .
N-1
k
Nyquist-Frequency: k=N/2
Offset/Bias: k=0
positive
negative
Notes: Positive and negative Frequenzen in der FFT

## Slide 8: FFT in Real-Time | Practical Issues: Frequency Resolution
Length of the signal
Length of the signal
Length of the signal
Length of the signal
Bin width:
Resolution
N-1
0 1 2 . . .
k
Notes: Length of the times signal: N Ts = N/Fs
T_1 = N Ts
T_2 = ½ T_1 = ½ N Ts
T_k = 1/k N Ts
Oder Kehrwert -> Frequenzen: f_k = k/N fs = k fs/N

## Slide 9: FFT in Real-Time | Simulink Example
Notes: c:\workspace\teachingSMC\FFT\Matlab\FFT4dSpace_rtKolloq_1.slx

## Slide 10: FFT in Real-Time | Simulink Example - Results
Ts = 1msec t_sim = 10 sec
Nyquist frequency
Notes: ~10 Runs: Simzeit = 10sec, 2^10 N à 1msec = 1Run takes ~1sec

## Slide 11: FFT in Real-Time | dSpace Example
Mdl: FFT4dSpace_1.slx
path: C:\workspace\teachingSMC\FFT\dSpace\SCALEXIO
Normalization of the amplitudes: - 1/N_samples - times 2: considering only half of the spectrum
⇝ 1/(N_samples /2)
Notes: C:\workspace\teachingSMC\FFT\dSpace\SCALEXIO

## Slide 12: FFT in Real-Time | dSpace Example
Mdl: FFT4dSpace_1.slx
path: C:\workspace\teachingSMC\FFT\dSpace\SCALEXIO
Notes: C:\workspace\teachingSMC\FFT\dSpace\SCALEXIO

## Slide 13: FFT in Real-Time | Summary
Analyzing a time domain signal in the frequency domain ⇝ Fourier Transform
The fast Fourier transform (FFT) is an efficient method to compute a discrete Fourier transform (DFT)
Nyquist frequency (highest frequency to be detected):
Frequency resolution (bin width):
One-sided FFT is sufficient if one is only interested in the identifying the frequencies
Use even number of samples N to have a clear Nyquist frequency:
Note considered here:
Leackage effect due to finite samples
Only one DSP Signal Processing License@Festo !
N-1
0 1 2 . . .
k
Quelle: https://de.wikipedia.org/wiki/Leck-Effekt (09.02.2024)
DFT
FFT
Calculation Effort DFT / FFT
⇝ ns ~31.2 years
⇝ ns ~30 sec

## Slide 14: FFT in Real-Time | Helpful Links
Eigensteve
  SteveBrunton_DFT
Matlab Tech Talks: Brian Douglas
  BrianDouglasMatlabTechTalk
How-to: FFT in a dSpace environment
  dSpace: FFT with ControlDesk
Notes: Steve Brunton University of Washington (Mechanical Engineering)

## Slide 16: FFT in Real-Time
Link to video: Steve Brunton / Matlab
Simulink Implementation
Plotting resutls from simulation and data capture…
How to chose:
  Sample Time Ts
  Number of samples for FFT : 2^N
  Bin Width (Frequenzauflösung)
  Nyquist Frequency
  Leackage effect
  ToDos: 09.02.2024
  - Bilder für ein/zwei seitiges Spektrum besser ausrichten…

## Slide 18: FFT in Real-Time | Discrete Fourier Transform (DFT)
Discrete-time signal
We are creating sines and cosines of different frequencies
https://www.youtube.com/watch?v=QmgJmh2I3Fw
Notes: https://www.overleaf.com/learn/latex/Using_colors_in_LaTeX
Skalarprodukt oder inneres Produkt von xn mit der k-ten Spalte…

## Slide 19: FFT in Real-Time | Practical Issues: one- / two-sided FFT
One-sided and two-sided FFT
Nyquist frequency
K=0
positive
One-sided
Nyquist frequency:
Nyquist frequency is the highest frequency which can be measured / detected in the
sampled data
0 1 2 . . .
N-1
k
Nyquist-Frequency: k=N/2
Offset/Bias: k=0
positive
negative
Notes: Nyquist Frequenz ist die höchste Frequenz die durch die FFT ermittelt werden kann